## Slide 1: OPG
Supervisor : Professor Dr Azian Bt Abd Aziz
Presenter : Mohamad Razlin Hamdani Bin Mohd Rafi

## Slide 2: ORTHOPANTOMOGRAM
*An OPG is a panoramic or wide view x-ray(dental radiography) of the lower facial structure, which displays all the teeth of the upper and lower jaw including the lower maxillary sinus and the arches of mandibular and their support structure on a single film.

## Slide 3: ANATOMY
Notes: TEMPORAL BONES: the side and base of the skull. Each consists 5 parts : squama, petrous, mastoid & styloid process
EAC (EXTERNAL AUDITORY CANAL)

## Slide 4: INDICATIONS
Impacted teeth
Third molar
Abnormality in OPG structure (supernumery teeth, wormian bone, polydontia, cyst and etc)
MVA (involving OPG structure)
Post op procedure

## Slide 5: EXAMPLE OF INDICATIONS
CYST
SUPERNUMERY TEETH

## Slide 6
MVA
IMPACTED TEETH

## Slide 7
X-ray unit : Planmeca Promax
LIST OF PROCEDURES DONE IN RADIOLOGY DEPARTMENT:
-OPG -CBCT(CONE BEAM COMPUTED TOMOGRAPHY) -LATERAL CEPHALOGRAM

## Slide 8: PATIENT PREPARATION
REMOVED:
JEWELLERIES DENTURES HAIR CLIP HEARING AIDS BROOCH SPECTACLES
*LMP FOR FEMALE
*WEAR LEAD APRON IS A MUST!

## Slide 9: PATIENT POSITIONING
Patient stand straight, adjust OPG unit height by adjusting buttons according to patients height related to patient’s chin on chin rest.
Grasp patient handles (cross hand) , step slightly forward, bite on BOTH grooves of the bite piece and place tongue to hard palate.
Laser beam light as indicator. Adjust layer light between patients lateral incisor and canine.
Patient head must straight to midsagittal plane light.
Select jaw shape and size accordingly.
Close temple support to ensure no movement during exposure.
Press exposure button at control console when it ready for exposure.

## Slide 10: INSTRUCTIONS
Patient should DO :
No swallowing.
Place tongue on hard palate.
Close lips during exposure.
Ensure no head movement while imaged being captured.

## Slide 11: EXAMPLE OF OPG IMAGE

## Slide 12
Thank You.